## Slide 1
WSN 2018 Project
Estimation of Feasibility for a 802.15.4 WSN
deployed on a medium sized boat
Fabio Peirano
Donato Brusamento

## Slide 2
Objective
Perform a quick feasibility test of a 802.15.4 ZigBee network in terms of packet loss and range, testing different materials as obstacles and 802.11 WiFi as external interference
Possible applications
Measurement of environment properties (ex: water temperature, wind direction/speed, sea current direction/speed)
Boat engine and control system parameters (ex: fuel level, engine temperature, rudder tilt)

## Slide 3
Idea: generate a 10k - packet burst:how many are lost?
Code: adaptation of BeeKit’s Connectivity Test with/without Repeater
A «dummy» repeater appends ‘-R’ to payloads and resends packets
Nodes accept only modified packets

## Slide 4
«Dummy»
Repeater (on battery)
Sender
(on serial)
Receiver
(on battery)
Peer to peer configuration (Coordinator – End Device)
Repeater configuration (Coordinator – Repeater – End Device)

## Slide 5
Scenarios
No WiFi interference
Repeater disabled
Repeater enabled
WiFi interference
Repeater disabled
Repeater enabled

## Slide 6
Channel selected: 12, with portable 802.11 Hotspots on Ch. 1
Fixed location of Sender: inside Helmsman’s cabin
Variable location of Receiver, repeater in the middle (when active)
Receiver locations of particular interest
Kind of ext. disturbances
Web browsing, uploading and downloading on 802.11 networks
EM noise caused by DC motors and electric equipment/tools, randomly switched on

## Slide 7
Performance Indicators
Max-Min LQI
Delay was always the same, about 0.0146 ms, as it was just simple and dirty
broadcast messaging .. (measured with WireShark)
Both calculated at Receiver: current number of packet was contained withing payload
No retransmission nor «complex» MAC mechanisms

## Slide 8
RESULTS

## Slide 9
No Repeater, No Interference
 | Packet Loss (%received) | Min LQI (dBm)
Engine Room | 9989/10000 | -72
Bow | 9822/10000 | -79
Aft | 9764/10000 | -84
Starboard Rail | 9271/10000 | -81
No Repeater, Interference
 | Packet Loss (%received) | Min LQI (dBm)
Engine Room | 9709/10000 | -76
Bow | 9373/10000 | -81
Aft | 9698/10000 | -84
Starboard Rail | 8595/10000 | -84

## Slide 10
Repeater, No Interference
 | Packet Loss (%received) | Min LQI (dBm)
Bow | 7332/10000 | -74
Aft | 6994/10000 | -71
Repeater, Interference
 | Packet Loss (%received) | Min LQI (dBm)
Bow | 7054/10000 | -79
Aft | 6686/10000 | -71
Top Deck | 5501/10000 | -51
Unfortunately there was
no time to do all tests
as there had been problems
with WireShark…and the owner
growing uneasy to return to his
beloved boat’s restauration.